## Slide 1
Software and Hardware Co-Optimization of GNN
汇报类型：组会
汇报人： | 刘洁琼
单位： | 华南理工大学
联系方式： | jqiongLiu@163.com

## Slide 2
1
Background
2
Related Works
3
Problem Definition
目 录
4

## Slide 3
Background
1

## Slide 4: Background
To find both GNN architectures with highest accuracy and hardware design with guaranteed performance (accuracy & efficiency)
High computational cost of GNN: 19G FLOPs on Reddit dataset[1]
The success of CNN co-optimization
Motivation
Large search space
Co-optimization strategy for DNN is not suitable for GNN
eg. FLOP efficiency of GNNs is 35% lower than VGG[2]
Target
Challenges
[1] Zhang Y , You H , Fu Y , et al. G-CoS: GNN-Accelerator Co-Search Towards Both Better Accuracy and Efficiency[J]. 2021.
[2] Zhihui Zhang, Jingwen Leng, Shuwen Lu, Youshan Miao, Yijia Diao, Minyi Guo, Chao Li, Yuhao Zhu: ZIPPER: Exploiting Tile- and Operator-level Parallelism for General and Scalable Graph Neural Network Acceleration. CoRR abs/2107.08709 (2021)

## Slide 5: Related Work Reference
GNN inference accelerators
  BoostGCN[1]: designed for certain GNN structure, and based on FPGA
G-NAS (GNN Network Architecture Search)
  GraphNAS[2]: based on Reinforcement Learning (only latency considered)
  EvlovingGCN[3]: based on Evolutionary Algorithm (only latency considered)
Hardware aware G-NAS
  FBNet[4]: high hardware cost
  Deepburning-g[5]: GNN network architecture not considered
Hardware-Software Co-Optimization
  G-CoS[6]: only considered accuracy as metrics
[1] B. Zhang, R. Kannan and V. Prasanna, "BoostGCN: A Framework for Optimizing GCN Inference on FPGA," 2021 IEEE 29th Annual International Symposium on FCCM, 2021
[2] Y. Gao et al., “Graphnas: Graph neural architecture search with reinforcement learning,” arXiv preprint arXiv:1904.09981, 2019
[3] G. Kyriakides and K. Margaritis, “Evolving graph convolutional networks for neural architecture search,” Neural Computing and Applications, 2021
[4] Bichen Wu et al. 2019. Fbnet: Hardware-aware efficient convnet design via differentiable neural architecture search. In Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition.
[5] S. Liang et al., “Deepburning-gl: an automated framework for generating graph neural network accelerators,” in ICCAD, 2020.
[6] Y. Zhang, H. You, Y. Fu, T. Geng, A. Li and Y. Lin, "G-CoS: GNN-Accelerator Co-Search Towards Both Better Accuracy and Efficiency," 2021 IEEE/ACM ICCAD, 2021

## Slide 6: Related Work
  Focus on specific GNN design instead of the design space
  Inefficient search process: 20000 networks-P100 GPUs require 4 days[1]
  Time performance & Hardware efficiency not considered
GNN inference accelerators
G-NAS (GNN Network Architecture Search)
Hardware aware G-NAS
  Assume fixed hardware design
  Explore architecture search space only
[1] W. Jiang et al., "Hardware/Software Co-Exploration of Neural Architectures," in IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, vol. 39, no. 12, pp. 4805-4815, Dec. 2020, doi: 10.1109/TCAD.2020.2986127.

## Slide 7
Problem Definition
2

## Slide 8: 本周工作
Neuro sim
找数据 (router, SRAM, CIM)
看accuracy模型

## Slide 9: Software Design Space
GNN Network Design Space:
  Intra-layer Design:
  Suppose L Layers in GNN，each L have m choices:
  Inter-layer Design
    2 kind of connection between adjacent layers
    Connection Type: C {Stack(0), Skip connections(1)}
  Configuration Parameters
    Learning Rate: LR {0.1, 0.01, 0.001};
    Optimizer: O {Adam, SGD}
Attributes | Type | Value
Batch Norm | Bool | 0/1
Dropout | enum | {0, 0.3, 0.6}
Activation | enum | {ReLU,LReLU}
Aggregation | enum | {Mean, Max, Sum}
Fig. A stack connection

## Slide 10: Hardware Design Space
Assumption: specialized device for GNN, use IMC
Hardware Design Space:
  Number of PEs in PE array: =
  Each PE has a Quantization rate q (related to computing time)
    N is the number of PEs
  Number of tile per chiplet:
  CIM(Computing in Memory) type: CIM type
  Buffer size of per chiplet: b
  Hardware topology: , is vertex set, is edge set (physical link)

## Slide 11: Decision Variables
GNN Network Structure
  GNN网络中共有n层结构，对每一层i，可选择
  B: Batch Normalization(bool), D: dropout ratio(double)
  ACT: activation(enum), AGG: aggregation(enum)
  C: inter layer connection, LR: learning rate, O: Optimizer Type
Mapping
  Divide GNN into multiple tasks
  Assign each task to each
Hardware
  Quantization rate:
  Hardware topology
  : the number of chiplet
  : the number of tile per chiplet
  b: buffer size for per chiplet
I1
I2
I3
I
I
I
PE
PE
PE
PE
Network
Structure
Task
Division
PE Set
PE
PE
PE
PE
Fig. task division and assignment

## Slide 12: Constraints
Area
  : area of total tiles
  : area of total routers
  : area of IO interface, accumulation unit, global buffer
Accuracy
  Acc(Gnet(B,D, ACT, AGG), q) (准确率与GNN网络结构和quantization相关)
  其中Acc是一个以[B, D, ACT, AGG, q]为自变量，GNN在目标数据集上的准确率accuracy为因变量的函数（拟合得到）
Power
  P

## Slide 13: Constraints-Accuracy
方法一：
  Acc(Gnet(B,D, ACT, AGG), q) (准确率与GNN网络结构和quantization相关)
  其中Acc是一个以[B, D, ACT, AGG, q]为自变量，GNN在目标数据集上的准确率accuracy为因变量的函数（拟合得到）
方法二：参考论文 ApproxANN[1]
  Neuron criticality analysis: a ranking vector for each neuron
  神经元个数
  定义一个总误差，其中每个神经元的重要性，通过梯度求得; 一个与quantization q相关的量
[1]ApproxANN: An Approximate Computing Framework for Artificial Neural Network

## Slide 14: Data for Constant Values
Area
  Power
Fig. information from dsent for routers
Fig. configuration information for IMC
Fig. information from cacti for SRAM

## Slide 15: Objective Function
解释
  生成任务图
    的权重为计算时间,
    两点之间的权重为节点之间的传输时间,
  求最长路，即图G的直径为总时间
    其中D为最长路径算法函数, s是最长路径P上的
    其中opi为第i层的操作，C是层间连接类型，lr是学习率，O是优化器选择
    H = {q, Nt, Nc, buf, T}, 其中q是quantization rate，Nt、Nc是chiplet个数和大小，buf是buffer size, T是硬件拓扑结构

## Slide 17
谢谢！
敬请批评指正！