## Slide 1
Software and Hardware Co-Optimization of GNN
汇报类型：组会
汇报人： | 刘洁琼
单位： | 华南理工大学
联系方式： | jqiongLiu@163.com

## Slide 2
1
Background
2
Related Work
3
Problem Definition
目 录
4

## Slide 3
Background
1

## Slide 4: Background
To find both GNN architectures with highest accuracy and hardware design with guaranteed performance (accuracy & efficiency)
High computational cost of GNN: 19G FLOPs on Reddit dataset[1]
The success of CNN co-optimization
Motivation
Large search space
Co-optimization strategy for DNN is not suitable for GNN
eg. FLOP efficiency of GNNs is 35% lower than VGG[2]
Target
Challenges
[1] Zhang Y , You H , Fu Y , et al. G-CoS: GNN-Accelerator Co-Search Towards Both Better Accuracy and Efficiency[J]. 2021.
[2] Zhihui Zhang, Jingwen Leng, Shuwen Lu, Youshan Miao, Yijia Diao, Minyi Guo, Chao Li, Yuhao Zhu: ZIPPER: Exploiting Tile- and Operator-level Parallelism for General and Scalable Graph Neural Network Acceleration. CoRR abs/2107.08709 (2021)

## Slide 5
Related Work
2

## Slide 6: Related Work Reference
GNN inference accelerators
  BoostGCN[1]: designed for certain GNN structure, and based on FPGA
G-NAS (GNN Network Architecture Search)
  GraphNAS[2]: based on Reinforcement Learning (only latency considered)
  EvlovingGCN[3]: based on Evolutionary Algorithm (only latency considered)
Hardware aware G-NAS
  FBNet[4]: high hardware cost
  Deepburning-g[5]: GNN network architecture not considered
Hardware-Software Co-Optimization
  G-CoS[6]: only considered accuracy as metrics
[1] B. Zhang, R. Kannan and V. Prasanna, "BoostGCN: A Framework for Optimizing GCN Inference on FPGA," 2021 IEEE 29th Annual International Symposium on FCCM, 2021
[2] Y. Gao et al., “Graphnas: Graph neural architecture search with reinforcement learning,” arXiv preprint arXiv:1904.09981, 2019
[3] G. Kyriakides and K. Margaritis, “Evolving graph convolutional networks for neural architecture search,” Neural Computing and Applications, 2021
[4] Bichen Wu et al. 2019. Fbnet: Hardware-aware efficient convnet design via differentiable neural architecture search. In Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition.
[5] S. Liang et al., “Deepburning-gl: an automated framework for generating graph neural network accelerators,” in ICCAD, 2020.
[6] Y. Zhang, H. You, Y. Fu, T. Geng, A. Li and Y. Lin, "G-CoS: GNN-Accelerator Co-Search Towards Both Better Accuracy and Efficiency," 2021 IEEE/ACM ICCAD, 2021

## Slide 7: Related Work
  Focus on specific GNN design instead of the design space
  Inefficient search process: 20000 networks-P100 GPUs require 4 days[1]
  Time performance & Hardware efficiency not considered
GNN inference accelerators
G-NAS (GNN Network Architecture Search)
Hardware aware G-NAS
  Assume fixed hardware design
  Explore architecture search space only
[1] W. Jiang et al., "Hardware/Software Co-Exploration of Neural Architectures," in IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems, vol. 39, no. 12, pp. 4805-4815, Dec. 2020, doi: 10.1109/TCAD.2020.2986127.

## Slide 8
Problem Definition
3

## Slide 9: Software Design Space
GNN Network Design Space:
  Intra-layer Design:
  Suppose L Layers in GNN，each L have m choices:
  Inter-layer Design
    2 kind of connection between adjacent layers
    Connection Type: C {Stack(0), Skip connections(1)}
  Configuration Parameters
    Learning Rate: LR {0.1, 0.01, 0.001};
    Optimizer: O {Adam, SGD}
Attributes | Type | Value
Batch Norm | Bool | 0/1
Dropout | enum | {0, 0.3, 0.6}
Activation | enum | {ReLU,LReLU}
Aggregation | enum | {Mean, Max, Sum}
Fig. A stack connection

## Slide 10: Hardware Design Space
Assumption
specialized device for GNN inference, using IMC (In Memory Computing)
Hardware Design Space:
  Number of PEs in PE array: =
  Each PE has a Quantization rate q (related to computing time)
    N is the number of PEs
  Number of tile per chiplet:
  CIM(Computing in Memory) type: CIM type
  Buffer size of per chiplet: b
  Hardware topology: , is vertex set, is edge set (physical link)

## Slide 11: Decision Variables
GNN Network Structure
  GNN网络中共有n层结构，对每一层i，可选择
  B: Batch Normalization(bool), D: dropout ratio(double)
  ACT: activation(enum), AGG: aggregation(enum)
  C: inter layer connection, LR: learning rate, O: Optimizer Type
Mapping
  Divide GNN into multiple tasks
  Assign each task to each
Hardware
  Quantization rate:
  Hardware topology
  : the number of chiplet
  : the number of tile per chiplet
  b: buffer size for per chiplet
I1
I2
I3
I
I
I
PE
PE
PE
PE
Network
Structure
Task
Division
PE Set
PE
PE
PE
PE
Fig. task division and assignment

## Slide 12: Constraints
Area
  : area of total tiles
  : area of total routers
  : area of IO interface, accumulation unit, global buffer
Accuracy
  , L是层数，Nl是第l层的神经元个数
  是第l层的剪枝误差
  是排序向量
  是与量化q有关的误差
Power
  P

## Slide 13: Data for Constant Values
*Intra-chip data
Area
  Power
Fig. information from dsent for routers
Fig. configuration information for IMC[1]
Fig. information from cacti for SRAM
Fig. information for RRAM[2]
[1] A Case for Emerging Memories in DNN Accelerators
[2]A Customized NoC Architecture to Enable Highly Localized Computing-On-the-Move DNN Dataflow
DRAM power: 9.75pJ/bit
  * MAC of different precision
  8-bit MAC : 135.1um2, 0.024pJ/op

## Slide 14: Data for Constant Values
  * Inter-chip data
  Energy:
  Delay(/cycle)
NN-Baton: DNN Workload Orchestration and Chiplet Granularity Exploration for Multichip Accelerators
Fig. information from NNBaton

## Slide 15: Constraints
Area
  Accuracy
  , L是层数，Nl是第l层的神经元个数
  是第l层的剪枝误差
  是排序向量
  是与量化q有关的误差
Power
  P
  (J/s)

## Slide 16: Constraints-Accuracy
  为每一层定义一个总误差
  , L是层数，Nl是l层神经元个数
  其中
  是剪枝带来的误差;
  是l层每个神经元的ranking vector，每个神经元的重要性，通过梯度求得 ;
  一个与quantization q相关的量;
  * 参考论文 Going Deeper with Embedded FPGA Platform for Convolutional Neural Network[1]
  在模型量化中，浮点数R可以表示为定点数 其中
  S和量化位数q有关 (* q可以针对data/weight)
  其中W的该神经元的权重（使用64位浮点表示），W’是W量化后的值
[1] Jiantao Qiu, Jie Wang, Song Yao, Kaiyuan Guo, Boxun Li, Erjin Zhou, Jincheng Yu, Tianqi Tang, Ningyi Xu, Sen Song, Yu Wang, and Huazhong Yang. 2016. Going Deeper with Embedded FPGA Platform for Convolutional Neural Network. Association for Computing Machinery, New York, NY, USA, 26–35.

## Slide 17: Constraints-Accuracy
  Network pruning factor，参考论文 Efficient DNN neuron pruning[1]
  按层剪枝（layer-wise）为每一层l定义mask为
  第L层的权重矩阵
  定义第l层剪枝后的输出为
  定义剪枝损失(NRE, Nonlinear Reconstruction Error)
  , 其中是 scaling factor, 是l层神经元个数
[1] Chunhui Jiang, Guiying Li, Chao Qian, and Ke Tang. 2018. Efficient DNN neuron pruning by minimizing layer-wise nonlinear reconstruction error. In Proceedings of the 27th International Joint Conference on Artificial Intelligence (IJCAI'18). AAAI Press, 2298–2304.
Fig. layer-wise network pruning

## Slide 18: Constraints-Accuracy
  * 参考论文 ApproxANN[1]
  其中t预测目标(𝑡𝑎𝑟𝑔𝑒𝑡), 𝑧是实际输出，c是通道个数
  分类计算每个神经元（，）的
  (1) 输出层neuron
  (2) 中间层neuron
  实现方式：修改2层的GCN
[1] Q. Zhang, T. Wang, Y. Tian, F. Yuan and Q. Xu, "ApproxANN: An approximate computing framework for artificial neural network," 2015 Design, Automation & Test in Europe Conference & Exhibition (DATE), 2015, pp. 701-706.
Fig. 神经元传播关系示意图

## Slide 19: Objective Function
解释
  生成任务图
    的权重为计算时间,
    两点之间的权重为节点之间的传输时间, ,l0是单位bit传输时间
  求最长路，即图G的直径为总时间
    其中D为最长路径算法函数, s是最长路径P上的
    其中opi为第i层的操作，C是层间连接类型，lr是学习率，O是优化器选择
    H = {q, Nt, Nc, buf, T}, 其中q是quantization rate，Nt、Nc是chiplet个数和大小，buf是buffer size, T是硬件拓扑结构

## Slide 21
谢谢！
敬请批评指正！